## Slide 1
and Innovating
Collaborating
Connecting,
40 Years of…

## Slide 2: Leveraging Machine Learning for Network Traffic Forecasting
Author,
Diane Onguetou, PhD
Independent Consultant
onguetou@umich.edu
Co-Author & Presenter,
Jeffrey Lee
Manager, Data Acquisition & Reporting
Rogers Communications
Co-Author,
Achintha Maddumabandara, P. Eng.
Principal Data Analyst
Rogers Communications

## Slide 3
AGENDA
Introduction
Case study
  The Network
  The Dataset
CAGR approach
  Global CAGR
  Global vs. local CAGR estimates
  Predictions from global vs. local CAGR
Machine Learning
  Seasonal decomposition
  Time series forecasting models
  Time series vs. CAGR forecasting
Key Insights
  Main improvements
  Challenges when applying ML
  Summary and recommendations

## Slide 4
Network Traffic Forecasting
  Traffic analysis
    [historical patterns, peak demand periods, seasonal variations]
  Growth projections
  Capacity planning
  Performance optimization
  Technology planning
Leveraging ML for Network Traffic Forecasting
  Captures complex patterns and dynamics in the data, leading to more effective resource management and improved network performance
  Automate iterative calculations and model attributes such as trends and seasonality, failure events, subsequent interactions between the primary and failover links, and network burst patterns
  Computational power to scale the analysis of multiple variables and high granularity
Main Objective
  Consider a large service provider network and sample traffic for 5 consecutive years
  Analyzes traffic patterns in the first four years and use insights and findings to predict traffic in the fifth year
INTRODUCTION

## Slide 5: Distribution of Connectivity at a Hubsite
CASE STUDY – The Network
Logical View

## Slide 6
CASE STUDY – The Dataset
From daily max to monthly P95, for half of the network links
60 months of historical data, 48 for training and 12 for comparison, i.e. [80, 20]

## Slide 7
CAGR APPROACH TO NETWORK TRAFFIC FORECASTING
How to determine global CAGR?
Sum up traffic across network
Fit in exp. reg.
Getting regression coefficients and :
Notes: Add how you derive CAGR from exponential regression line

## Slide 8: Limitations
CAGR APPROACH TO NETWORK TRAFFIC FORECASTING
Logic behind the choice of reference month
  Most recent measurement on hands
  vs. min/average/max over past 12 months
CAGR model accuracy
Applying a total-traffic CAGR to individual contributors
  Global vs. local CAGR estimates
  Predictions from global vs. local CAGR approaches (next slide)
Global vs. Local CAGR
2/3rd of local CAGRs are quite distant from global estimate

## Slide 9
CAGR APPROACH TO NETWORK TRAFFIC FORECASTING
CAGR is sensitive to period choice.
Most of the time, local CAGR provides a better performance

## Slide 10: Example of Internal Longhaul Link (multiplicative)
ML | Seasonal Decomposition
Total Traffic
(additive decomposition)

## Slide 11
Seasonal Decomposition (STL)
  Breaks down a time series data into its fundamental components (i.e. trend, seasonality, and residual) to better understand underlying patterns
Seasonal autoregressive integrated moving average (SARIMA)
  Combines autoregressive, differencing, and moving average components along with seasonal components to handle data with both non-seasonal and seasonal patterns
Holt-Winters/Exponential Smoothing (ETS)
  Uses weighted average of past observations to predict future values, considering trend, seasonality, and level components to make accurate predictions for time series data
ML | Example of Time Series Forecasting Models

## Slide 12: Example of Internal Metro Link (multiplicative)
ML | Seasonal Decomposition
Example of International Link (additive)

## Slide 13
ML | Time Series Forecasting Models [longhaul link]
Holt-Winters has the best performance here
SARIMA seems to simply shift and repeat previous behavior, but still better than exp. reg.

## Slide 14
ML | Time Series Forecasting Models [international link]
Holt-Winters and SARIMA seem to show an equivalent performance here
Exp. reg. still has the worst performance

## Slide 15
ML | Time Series Forecasting Models [metro link]
Holt-Winters better and more consistently across links
SARIMA seems to simply shift and repeat previous behavior, most of the time still better than exp. reg.

## Slide 16
CHALLENGES WHEN ADOPTING ML-BASED TRAFFIC MODELLING
Access to clean dataset is our biggest challenge!!!
Forced to do an [80,20] where the ideal is [90,10] for training and test sets

## Slide 17
Good practices
  Invest in quality datasets
  Choose models appropriate to your needs
  Re-evaluate models in a regular basis and track your progress
If CAGR simplicity is still appealing and fits current needs
  Plenty of tools allow to easily build ML pipeline that can support distributed CAGR
  Build a strategy behind the reference value to which the growth factor is applied
  CAGR is tied to time series trend and does not consider seasonality that is more likely to be present in your data
Beyond CAGR…
  Do not be intimidated by the term machine learning.
  Python and R languages offer appropriate libraries that facilitate ML model training and testing
  ML proposes simple and effective models for seasonal decomposition of time series
  ML time series models capture both trend and seasonality for better forecasting
  SARIMA requires parameter tuning to perform
  Holt-Winters is simple enough and shows better results for our use case
KEY INSIGHTS

## Slide 18: Thank you to my co-author: Achintha Maddumabandara, P. Eng. Principal Data Analyst Rogers Communications
Diane Onguetou, PhD
Independent Consultant
onguetou@umich.edu